## Slide 1: 3.5 GHz Waveform Generation for Testing and Development of ESC Detectors
Raied Caromi, John Mink, Michael Souryal
{raied.caromi, john.mink, michael.souryal}@nist.gov
WInnComm Nov. 2017

## Slide 2: Background
Citizens Broadband Radio Service (CBRS) allows spectrum sharing in 3550 MHz – 3700 MHz band between federal and commercial users, in accordance with FCC rules
Environmental Sensing Capability (ESC) detects and reports the presence of federal incumbent radar signals in these bands
ESC sensors will not have full knowledge of radar waveform parameters such as pulse repetition, pulse duration and center frequency of the incumbent radar
Field-measured waveforms include channel propagation effects such as time-varying multipath fading and pulse dispersion
Utilize field-measured radar waveforms and computer generated interference signals to generate waveforms similar to what an actual ESC sensor will observe
Develop open source code for framework, signal processing blocks and GUI generation tool
The waveforms and their parameters can be used by ESC applicants and developers for training and testing incumbent radar detection algorithms

## Slide 3: Examples of field-measured radar waveforms
Figure 3.1 , NASCTN Report 2, NIST Technical Note 1954, 3.5 GHz Radar Waveform Capture at Point Loma, Final Test Report,
https://doi.org/10.6028/NIST.TN.1954
Magnitude of an IQ capture of a typical 3550 MHz SPN43 radar. The full capture epoch of just over 60 s duration is shown here.

## Slide 4: Examples of field-measured radar waveforms
Figure 3.8, NASCTN Report 2, NIST Technical Note 1954, 3.5 GHz Radar Waveform Capture at Point Loma, Final Test Report,
https://doi.org/10.6028/NIST.TN.1954
Spectrogram of a SPN-43 signal with temporal fading, captured with the omni-directional antenna showing spread of peak rotation power of 31.5 dB, while the mean peak power, pooled over all rotations in this capture, is -54.6 dBm.

## Slide 5: Examples of field-measured radar waveforms
Figure 3.18 , NASCTN Report 2, NIST Technical Note 1954, 3.5 GHz Radar Waveform Capture at Point Loma, Final Test Report,
https://doi.org/10.6028/NIST.TN.1954
Spectrogram showing broadband noise from Radar 3. Note that SPN-43 peaks at 3550 MHz are visible earlier than 30 s, but are hidden by interference at later times.

## Slide 6: Waveform generation framework
Define basic objects to handle signal input/output from/to files
Read signals in terms of segments of samples
Perform signal processing procedures on the segment of samples
Track signal timing, end of file action, IQ format and scaling
Signal processing procedures are built on top of the basic framework
GUI to visualize the resulting waveforms and to automate the process of generating the waveforms
The GUI utilizes the framework and the waveform signal processing blocks to mix up to two radar, one adjacent band interference (ABI), and two LTE signals
The GUI simplifies the selection of certain parameters such as signal power levels, and randomizes other parameters such as start time, and frequency
The software automates the generation of multiple waveform files

## Slide 7: Read and write complex baseband signals
All signals are saved as integer 16-bit interleaved I/Q data file to minimize disk storage size
Signal from file: read a segment of samples from a signal file and prepare it for baseband processing
Signal to file: write a segment of samples to a file
A waveform object can have one or more (signal from file)/(signal to file) objects

## Slide 8: Multi-task execution
Organize multi-task execution
Manage the type of the execution, i.e., sequential or parallel.

## Slide 9: Signal preprocessing and measurement preparations
Certain tasks are performed before waveform generation
Decimation is performed on the original radar waveforms to extract clean radar signals centered at zero Hz baseband
Instantaneous signal to interference ratio (SIR) calculation during the generation process requires estimation of radar peaks and their times at every sweep
LTE TDD signals are simulated and up-sampled to the final waveform sampling rate beforehand
Real captured LTE TDD signals can also be used instead of the synthetically generated LTE signals

## Slide 10: Decimation process
The field-measured radar waveforms are sampled at 225 MHz and are about 60 seconds long
Each waveform is shifted with an offset frequency so that the radar is set at zero baseband center frequency
An antialiasing low-pass filter is applied
The signal is then down-sampled to 25 MHz and saved to a file
The waveform is processed in segments due to large size of the file

## Slide 11: Decimation execution
The decimation executor handles the task of processing multiple files
To reduce the run time, the waveform files are processed in parallel

## Slide 12: Waveform signal processing
Creates an object with multiple signals (signal from file) and output signal (signal to file)
Three types of signal files (radar, ABI, LTE with channel effect)
Number of each signal type
Parameters of each signal
Generate a waveform segment for preview
Generate full waveform up to total time and save to a file and measure the instantaneous SIR

## Slide 13: Waveform object example
An example of a waveform object used by the waveform generator with certain waveform parameters:
90-second waveform with two radars starting at 5 seconds and 11 seconds
Gains are set according to desired power levels
After the generation process all the object parameters, instantaneous SIR values, and signal sources are saved in JSON format for easy access

## Slide 14: Waveform generation
Handles multiple waveform generation process sequentially or in parallel
Tracks waveform parameters
Tracks signals sources and output files

## Slide 15: GUI waveform generation
The GUI provides a convenient way to access all the generation parameters
Select signal sources
Change frequencies, gains, turn ON/OFF signals
Instantaneous preview of the waveform
Set specific power levels, or desired SIR
Generate parameters by randomization or with predefined intervals
Generate multiple waveform files

## Slide 16: Signal Sources Panel
Select signal source paths
Add desired files to the selection boxes
Selected files will be used for waveform preview and single file generation

## Slide 17: Waveform Preview Panel
The GUI mixes two radar signals, one ABI signal, two LTE signals with different channel settings, and an optional AWGN signal
Preview panel provide access to all signal parameters (Status, Gain, Frequency)
Demonstrates the waveform before the generation process
Estimate gains based on the desired power levels or target SIR
Access to spectrum analyzer/ spectrogram and time scope during preview

## Slide 18: Waveform Generation Panel
Load all the preview parameters in one place
Provide capability to edit/modify parameters in one place
Generate single or multiple files
Turn On/Off parallel processing

## Slide 19: Waveform Preview Demonstrations
For the purpose of this demonstration, we use a synthetically generated radar signal
Two radar signals at -5 MHz and +5 MHz and One LTE TDD centered at 0 Hz

## Slide 20: Waveform Preview Demonstrations
Spectrum of two LTE TDD signals with one radar signal at the center
Spectrum/ Spectrogram/ and time scope panels keeps previewing the waveform while the engine keeps sampling and mixing the signals until the end of the preview time

## Slide 21: Waveform Preview Demonstrations
Spectrogram of the waveform
Radar at zero center frequency
The LTE channel was turned ON in the middle of the preview process

## Slide 22: Waveform Preview Demonstrations
Time scope showing the LTE TDD signals and the radar signal pulses

## Slide 23: Concluding Remarks
CBRS spectrum sharing requires ESC sensor deployment to detect and report the presence of federal incumbent radar
Some characteristics of the actual incumbent radar signals are difficult to generate
Utilize field-measured radar waveforms
Waveform generation with certain power levels or SIR values for testing and development of incumbent radar detection algorithms
Framework and signal processing block to handle signal mixing and generation process
GUI to demonstrate the waveform and automate the generation process
The GUI tool is deployable and can run without licensed software

## Slide 24
Questions?
Source Code: https://github.com/usnistgov/ESCWaveformGenerator.git
Contacts: Raied Caromi, raied.caromi@nist.gov
John Mink, john.mink@nist.gov
Michael Souryal, michael.souryal@nist.gov