## Slide 1
Hands-on Learning for Novel Solutions to Radio Spectrum Problems Using Remote Laboratory Exercises and Tutorials for Spectrum-agile Radio Frequency Systems

## Slide 2
2328-US Navy Hovercraft - this image by flightzone is licensed under a Creative Commons Attribution 3.0 Unported License. http://www.freeimageslive.co.uk/free_stock_image/hovercraftinflightjpg
Web-based Visualization
Experiment Management
(CRTS)
Software-defined Radio Testbed (CORNET)
Internet
Radio Controller Code
and Configuration
Engineering Students/
STEM Professionals
15.2 Mbps
Performance
Reporting
Hands-on
Tutorials
Student image: https://www.biologycorner.com/2013/08/03/classroom-collaboration-tools/
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.

## Slide 3
Goals
The intended use of the tutorials is to teach / review and demonstrate radio adaptation techniques using cognitive radio (CR) systems that can be controlled by logging into a remote software-defined radio (SDR) - based testbed
This will be useful for anyone interested in learning, reviewing, teaching, demonstrating, or researching technical concepts related to spectrum sharing and cognitive radio.

## Slide 4: Specific Goals
Encourage those interested in spectrum sharing and CR to utilize our free available resources.
Allow the users to familiarize themselves with the software while applying changes in radio parameters
  such as frequency, transmitted power, modulation type, error correction coding type, and packet length.
Encourage user to feel comfortable enough to conduct their own experiments.
Gather feedback from tutorial participants to help improve the lessons and expand features (hardware and software) in the testbed to accommodate participants' educational and research requirements.

## Slide 5: Available Resources
Available resources:
  The Cognitive Radio Network Testbed (CORNET)
  The Cognitive Radio Test System (CRTS)
  CORNET 3D
CORNET is a network of software-defined radios which can be remotely accessed from most Internet-connected computers
CRTS provides a flexible framework for over the air test and evaluation of (CR) networks
CORNET 3D is a web-based spectrum visualization software where the users can monitor the statuses of nodes

## Slide 6: CORNET
CORNET testbed consists of 48 software-defined radio nodes, all remotely accessible
Notes: The original CORNET testbed consists of 48 software-defined radio nodes, all remotely accessible.
Node location is along the hallways of Kelly Hall/ICTAS building, 12 nodes per floor.
The user access is free, only needs registration
We have an FCC experimental license for several bands.
LDAP: lightweight directory access protocol -- for creating and managing user accounts, nodes, etc.
NFS: Network file system -- shared user folder accessible from any node
Image server: to reimage each or all SDR nodes
USRP model: USRP generation 2 with WBX daughterboard (50 MHz - 2200 MHz)
SDR processor: XEON Dal-core server (2009)

## Slide 7: CORNET
CORNET nodes are located in Kelly Hall of the main campus of Virginia tech in Blacksburg, VA
Notes: The original CORNET testbed consists of 48 software-defined radio nodes, all remotely accessible.
Node location is along the hallways of Kelly Hall/ICTAS building, 12 nodes per floor.
The user access is free, only needs registration
We have an FCC experimental license for several bands.
LDAP: lightweight directory access protocol -- for creating and managing user accounts, nodes, etc.
NFS: Network file system -- shared user folder accessible from any node
Image server: to reimage each or all SDR nodes
USRP model: USRP generation 2 with WBX daughterboard (50 MHz - 2200 MHz)
SDR processor: XEON Dal-core server (2009)

## Slide 8: CORNET-3D
Web Browser
CORNET3D
CORNET3D
Web Gateway
SDR Nodes:
Spectrum Sensing
CTRS Scenarios
HTML5 + X3D
User Interface
Web server
TCP
TCP
TCP
TCP
WebSockets
cornweb
Frontend
Backend
Notes: Frontend: browser @user terminal
Backend: Python Web Server runs on CORNWEB, relays information
Keeps track of experiments
CRTS: on SDR node (C++)
Controller can run anywhere in the SDR Nodes

## Slide 9: CORNET-3D
CORNET-3D can be used to visualize tests as they happen and allows for human control of the radios which can be useful for tutorials
3D visualization of spectrum
Notes: Frontend: browser @user terminal
Backend: Python Web Server runs on CORNWEB, relays information
Keeps track of experiments
CRTS: on SDR node (C++)
Controller can run anywhere in the SDR Nodes

## Slide 10: CRTS
CRTS is an open source software that enables development and testing of CR networks
Users can define testing scenarios involving a number of CR’s as well as interferers
Results and metrics can be visualized using octave/MATLAB logs automatically generated during experiment

## Slide 11: Thank You
Comments?
Questions?